## Slide 1: Announcements Monday 9/9
Prof. Higgins is assigning a lab prep, check the “Lab 2” folder on Moodle.
Blog response (shorter than a post) due on Friday by 11:59pm
Quizz Prep Doc, due as extra credit hw by Wednesday 9/11 5pm
Problem Set 2 posted; due Wed 9/18 in class—it’s long!
Exam blueprint (partial) for Midterm-1 posted. Note I will add to doc as we cover material. Will be finalized one week before exam.

## Slide 2: Chapter 1 (course notes) Characteristics of Water
Physical
Chemical
Biological

## Slide 3: Physical Characteristics of Water (in your notes)
Turbidity
Solids or Particles
Color
Taste and odor
Temperature

## Slide 4: Physical Characteristics 1.Turbidity
Optical clarity of water, resulting from light scattering by particles (high turbidity = “cloudy” or “hazy” water)
Reported in units of nephelometric turbidity units (NTU)
Good indicator of presence of harmful microorganisms
WHO standard < 5 NTU
U.S. standard < 0.3 NTU 95% of the time, never higher than 1 NTU

## Slide 5: 2. Particles or Solids
Total Solids TS
  Sample dried at 103-105 ºC
Total Suspended Solids TSS
  sample filtered, sample retained on filter dried
Total Dissolved Solids TDS
  sample filtered, filtrate dried

## Slide 6: Total Solids = Fixed Solids + Volatile Solids
Dried solids are combusted at 550 ºC:
  Fixed Solids FS (inorganic, ash)
  Volatile Solids VS (organic)

## Slide 7: TSS = FSS + VSS
Dried solids retained on filter are combusted at 550 ºC:
  Fixed Suspended Solids FSS (inorganic, ash)
  Volatile Suspended Solids VSS (organic)

## Slide 8: TDS = FDS + VDS
Dried solids that passed through filter are combusted at 550 ºC
  Fixed Dissolved Solids FDS (inorganic, ash)
  Volatile Dissolved Solids VDS (organic)

## Slide 9: I. Physical Characteristics
3. Color: Dissolved organic matter, metal ions (e.g. Fe and Mn), and turbidity
4. Taste and Odor: Dissolved organic and inorganic matter, microorganisms, water treatment process
5. Temperature: important because controls rates of reactions. In winter: 0.5 to 3 oC; in summer: 2 to 25 oC

## Slide 10: II. Chemical Characteristics
Inorganic (Table 10.4, p. 402; Table 10.8, p.408):
  calcium and magnesium in surface water,
  chloride from saltwater intrusion,
  fluoride, NO32-, iron, manganese, and sulfur in surface water and groundwater
Organic (Table 10.8, p. 407):
  Synthetic, or man-made, organics—e.g fuels, cleaning solvents, pesticides
  Emerging chemicals of concern: personal care products & pharmaceuticals

## Slide 11: III. Biological Characteristics
Pathogens microorganisms that cause disease.
  viruses, bacteria, protozoa, helminth (round worm)
  EPA monitors for indicator organisms—coliforms—that are not pathogens, but are present in mammals and easy to detect and measure.
    U.S. EPA standard < 1 coliform per 100 mL